OpenWRT MiniEMBWifi Dev Build
Purpose
Install OpenWrt distribution as a build environment without the Lua web interface and not as a router but as more of a general purpose device
Build fresh install of firmware
Capability to develop in other languages
Supporting libraries for minimal development
Retain capabilities of on-board peripherals

---
Hardware
 Ralink RT3050 based board
 MIPS 24KEc 320 Mhz CPU
 1 UART serial port
 8MB NOR Flash
 32MB DRAM
 1 USB2.0 port
 1 WAN/LAN Port 10/100M
 1 WLAN 802.11a,b,g access point or station modes
 Operating Temperature: 0 – 50 Deg Celsius, Storage: -20 – 50 Deg Celsius
 Certification: FCC, CE
 USB to Serial 4-PIN header for programming/serial console
 Antenna 3dBi Dipole detachable antenna
 Power Adaptor 5 V 2.5 Amps

---
Software
Host System
Ubuntu 12.04 32-bit Linux 3.2.60-generic kernel
Target Build System
ATTITUDE ADJUSTMENT (Attitude Adjustment, r40877) OpenWrt 12.09 Linux 3.3.8
* OpenWrt is a custom embedded linux distribution integrated with buildroot
eliminating need to find correct package combinations when cross-compiling
       for example
1. svn co svn://svn.openwrt.org/openwrt/branches/attitude_adjustment
2. Added following lines to feeds.conf in main source directory:
src-svn packages svn://svn.openwrt.org/openwrt/branches/packages_12.09
src-svn xwrt http://x-wrt.googlecode.com/svn/trunk/package
3. According to README file in main source directory:
./scripts/feeds update -a
./scripts/feeds install -a
   Brings in all packages from sources in feeds.conf

---
4. make menuconfig
* menu abbreviated for brevity
5. make
make[1] world
 make[2] target/compile
 make[3] -C target/linux compile
. . . .
OpenWRT 3,10.36
BARRIER BREAKER (Bleeding Edge, r40891)
 Linux Kernel 3.10.18
 -----------------------------------------------------
 OpenWrt BARRIER BREAKER (Bleeding Edge, r38695)
 -----------------------------------------------------

---
Kernel Build Options
CONFIG_KERNEL_DEBUG_FS=y
# CONFIG_KERNEL_PERF_EVENTS is not set
# CONFIG_KERNEL_PROFILING is not set
# CONFIG_KERNEL_KALLSYMS is not set
# CONFIG_KERNEL_FTRACE is not set
# CONFIG_KERNEL_DEBUG_KERNEL is not set
# CONFIG_KERNEL_DEBUG_INFO is not set
# CONFIG_KERNEL_AIO is not set
CONFIG_KERNEL_MAGIC_SYSRQ=y
CONFIG_KERNEL_ELF_CORE=y
# CONFIG_KERNEL_PROVE_LOCKING is not set
CONFIG_KERNEL_PRINTK_TIME=y
CONFIG_USES_SQUASHFS=y
CONFIG_TARGET_ROOTFS_JFFS2=y
CONFIG_TARGET_ROOTFS_SQUASHFS=y
CONFIG_TARGET_OPTIMIZATION=-Os -pipe -mips32r2 -mtune=24kec -fno-caller-	saves -mdsp”
CONFIG_SOFT_FLOAT=y
CONFIG_GCC_VERSION=”4.7.0”
CONFIG_ULIBC_VERSION=”0.9.33.2”
CONFIG_USE_UCLIBCXX=y
CONFIG_GPIO_SUPPORT=y
CONFIG_USB_SUPPORT=y
CONFIG_mipsel=y
CONFIG_ARCH="mipsel"

---
Toolchain
 BARRIER BREAKER (Bleeding Edge, r40891)
 Linux Kernel 3.10.18
 -----------------------------------------------------
 OpenWrt BARRIER BREAKER (Bleeding Edge, r38695)
 -----------------------------------------------------

---
Installed Packages
binutils - 2.22-5
busybox - 1.19.4-6
dropbear - 2011.54-2
hostapd - 20131120-1
hotplug2 - 1.0-beta-4
iptables - 1.4.10-5
iw - 3.6-1
jshn - 2013-10-19
kmod-button-hotplug - 3.3.8-3
kmod-cfg80211 - 3.3.8+2014-01-23.1-1
kmod-crypto-aes - 3.3.8-1
kmod-crypto-arc4 - 3.3.8-1
kmod-crypto-core - 3.3.8-1
kmod-eeprom-93cx6 - 3.3.8-1
kmod-fs-ext4 - 3.3.8-1
kmod-fs-vfat - 3.3.8-1
kmod-hid - 3.3.8-1
kmod-input-core - 3.3.8-1
kmod-input-evdev - 3.3.8-1
kmod-input-gpio-keys-polled - 3.3.8-1
kmod-input-polldev - 3.3.8-1
kmod-ipt-conntrack - 3.3.8-1
kmod-ipt-core - 3.3.8-1
kmod-ipt-nat - 3.3.8-1
kmod-ipt-nathelper - 3.3.8-1
kmod-leds-gpio - 3.3.8-1
kmod-ledtrig-usbdev - 3.3.8-1
kmod-lib-crc-ccitt - 3.3.8-1
kmod-lib-crc-itu-t - 3.3.8-1
kmod-lib-crc16 - 3.3.8-1
kmod-mac80211 - 3.3.8+2014-01-23.1-1
kmod-nls-base - 3.3.8-1
kmod-nls-cp437 - 3.3.8-1
kmod-nls-iso8859-1 - 3.3.8-1
kmod-ppp - 3.3.8-1
kmod-pppoe - 3.3.8-1
kmod-pppox - 3.3.8-1
kmod-rt2800-lib - 3.3.8+2014-01-23.1-1
kmod-rt2800-mmio - 3.3.8+2014-01-23.1-1
kmod-rt2800-soc - 3.3.8+2014-01-23.1-1
kmod-rt2x00-lib - 3.3.8+2014-01-23.1-1
kmod-rt2x00-mmio - 3.3.8+2014-01-23.1-1
kmod-scsi-core - 3.3.8-1
kmod-usb-core - 3.3.8-1
kmod-usb-hid - 3.3.8-1
kmod-usb-ohci - 3.3.8-1
kmod-usb-rt305x-dwc_otg - 3.3.8-1
kmod-usb-storage - 3.3.8-1
libblkid - 2.21.2-1
libblobmsg-json - 2013-10-19
libc - 0.9.33.2-1
Libgcc – 4.7.0-1
libip4tc - 1.4.10-5
libjson-c - 0.11-2

---
Installed Packages Cont.
libmount - 2.21.2-1
libnl-tiny - 0.1-3
libopenssl - 1.0.1g-1
librpc - 0.9.32-rc2
librt - 0.9.33.2-1
libubox - 2013-10-19
libubus - 2013-08-08
libuci - 2013-06-11.1-1
libuuid - 2.21.2-1
libxtables - 1.4.10-5
lsof - 4.86-1
netifd - 2013-07-16
objdump - 2.22-5
opkg
ppp - 2.4.5-10
ppp-mod-pppoe - 2.4.5-10
python-mini - 2.7.3-2
sed - 4.2.1-1
ubus - 2013-08-08
ubusd - 2013-08-08
wget - 1.13.4-1
wireless-tools - 29-5
wpad-mini - 20131120-1
zlib - 1.2.7-1

---
Final Build

---
Final Build Cont.

---
Final Build Cont.

---
Final Build Cont.

---
Network Working

---
Python Working

---
Previous Build

---
Previous Build Cont.

---
Problems and Resolution
Many problems but the greatest one:
1. Finding an image that worked correctly
First I tried the “Bleeding Edge” distribution like indicated in the guide.
I had problems with the image generating only a squashfs filesystem.
I took it upon myself to download the “Attitude Adjustment” distribution as indicated on openwrt.org.
After sucessfully building and indicating in the menuconfig both a squashfs, jffs2 filesystem be built, I found a testable image.
I tested it by loading it into RAM first as indicated below:

---
Results
I found by using the squashfs, jffs2 image with “attitude adjustment” worked and I could actually edit the filesystem and have it stay persistent.

---
References
- www.openwrt.org
http://www.omnima.co.uk/store/catalog/MiniEMBWiFi-p-16180.html